ModSpec: Introduction and Tutorial
updated 2012/11/06
Jaijeet Roychowdhury
[Speaker Notes: Notes here]

---
ModSpec: Motivation and Goals
- Verilog-A CME is lacking in several respects
  - too EE (semiconductor device) centric; weird un-aesthetic syntax
    - does not expose DAE API of devices transparently
  - VA-CME “standard” fragmentation? turf wars between companies?
    - want something GPL'd: no patents!
  - VA-CME has no support for bias-dependent noise, initialization hooks (?), limiting hooks, convergence criterion hooks, scaling, etc.
  - no support for parsing/netlist syntax info, time-dependence?
- VA-CME has inadequate open-source toolchain
  - ADMS: horrible structuring → limping for a decade
    - lacks support for internal current variables (Tom R. added this?)
  - is it really open-source? Laurent LeMaitre is now a company?
- Don't want device limited to specific network eqn. formulation (eg, MNA) – should support any network formulation
- Want genuinely domain-agnostic core device specification format (ie, should work for EE, reactions, etc.)
  - and should be able to “naturally” define elements spanning different domains
[Speaker Notes: username: 219Afall2011 password: 1Matlab0C++]

---
Outline
- ModSpec illustrated using:
  - electrical networks and devices
  - bio-chemical reaction networks and devices
- YET TO DO:
  - Reaction-electrical interface devices
    - eg, biosensors
  - Signal flow networks and devices
  - Mechanical networks and devices
    - SUGAR netlist concepts: good enough?
  - Fluidic networks and devices
    - eg, for chemical energy networks
  - Optical networks and devices

---
EE Networks: A Quick Recap
- EE Network Layer
  - nodes
    - there is a special node called ground
  - devices connect to nodes using branches
  - network-level unknowns
    - each non-ground node contributes one node voltage unknown
    - each branch contributes (in principle):
      - one branch current unknown
      - one branch voltage unknown
        - directions indicate current direction and branch voltage polarity
  - network-level equations
    - each non-ground nodes contributes one KCL equation
      - eg, KCLN:
    - each branch contributes one KVL equation:
      - (each branch also contributes one BCR equation – from the device layer)
- EE device layer
  - each can contribute several branches (connected to network-level nodes)
    - devices have access to network-level branch quantities ONLY
  - each device contributes one BCR equation for each of its branches:

---
A Generic Device (not limited to EE)
Device's Network Interface Layer
(interfaces device to network level)
Network
Level
n3
n1
n2
Network interface layer interfaces “network quantities” (eg, node voltages, node KCL current contribs) with “device quantities” (eg, branch voltages and currents)
Core Device
(eg, only branch
quantities and
int. quantities)

---
Core vs NIL vs Network Level
- Core device
  - relates (its own) branch voltages and currents (I/Os)
    - ie, supplies equations relating branch voltages/currents
  - may also contribute internal unknowns
    - these don't interact with network level quantities
    - for each internal unknown, device supplies one equation
- Network Level
  - contributes node voltage unknowns
  - sets up KCL equations for each node
    - using each device's Network Interface Layer
- Network Interface Layer
  - relates core device's I/Os (branch voltages/currents) to network level quantities (node voltages, node KCL contribs)
  - does not access core device's internal unknowns
Network Level
n1
3 nodes/KCL eqns
2 KVL eqns
n2
4 I/Os
2 eqns
Network Interface
Layer
3 device I/O to network KCL contrib. eqns
3 node KCL contribs.
3 node voltages
n3
Core
2 branches

---
Core Device: Basic Notions
- Each device:
  - has several inputs/outputs; some outputs provided explicitly, others implicit
  - contributes several internal unknowns
  - contributes several equations
- IOs: these are the Inputs/Outputs
  - 2n of them. (What is n? # of “core I/O eqns”; eg, # branches)
    - l of these can be designated ExplicitOutputs
      - stored in
    - the remaining 2n-l are called OtherIOs
      - stored in
- There can also be m InternalUnknowns (stored in )
- Equations: total of n+m equations supplied by device
    - l of these provide the ExplicitOutputs explicitly:
      - l equations: : qe(), fe()
    - the remaining n+m-l equations can be fully implicit:
      - n+m-l equations: : qi(), fi()
    - is a vector of time-varying functions, of length

---
Example: Resistor
- Explicit current output formulation
  - n=1; 2n = nIOs = 2
  - l=1 (ib is an explicit output) → ,
  - m=0 (no internal unknowns)
  - only 1 (explicit-output) equation:
- Implicit current formulation
  - n=1; 2n = nIOs = 2
  - l=0 (ib is implicit) →
  - m=0 (no internal unknowns)
  - only 1 (implicit) equation:
- EE Network Interface Layer
  - nn = n+1 = 2 nodes

---
Example: Capacitor (charge formulation)
- Charge formulation, explicit output
  - n=1; 2n = nIOs = 2
  - l=1 (qb is an explicit output) → ,
  - m=0 (no internal unknowns)
  - only l=1 (explicit) equation:
- Charge formulation, implicit
  - n=1; 2n = nIOs = 2
  - l=0 (no explicit output) →
  - m=0 (no internal unknowns)
  - only n+m-l=1 (implicit) equations:
- EE Network Interface Layer
  - nn = n+1 = 2 nodes
  - 2nn=4 NIF unknowns: nn=2 node voltages, nn=2 node currents:
  - n + nn= 3 equations:

---
Example: Capacitor (current formulation)
- Current formulation, explicit output
  - n=1; 2n = nIOs = 2
  - l=1 (qb is an explicit output) → ,
  - m=0 (no internal unknowns)
  - only l=1 (explicit) equation:
- Current formulation, implicit
  - n=1; 2n = nIOs = 2
  - l=0 (no explicit output) →
  - m=0 (no internal unknowns)
  - only n+m-l=1 (implicit) equations:
- EE Network Interface Layer
  - nn = n+1 = 2 nodes
  - 2nn=4 NIF unknowns: nn=2 node voltages, nn=2 node currents:
  - n + nn= 3 equations:

---
Example: Inductor (flux formulation)
- Flux formulation, explicit output
  - n=1; 2n = nIOs = 2
  - l=1 (fb is an explicit output) → ,
  - m=0 (no internal unknowns)
  - only l=1 (explicit) equation:
- Flux formulation, implicit
  - n=1; 2n = nIOs = 2
  - l=0 (no explicit output) →
  - m=0 (no internal unknowns)
  - only n+m-l=1 (implicit) equations:
- EE Network Interface Layer
  - nn = n+1 = 2 nodes
  - 2nn=4 NIF unknowns: nn=2 node voltages, nn=2 node currents:
  - n + nn= 3 equations:

---
Example: Inductor (voltage formulation)
- Voltage formulation, explicit output
  - n=1; 2n = nIOs = 2
  - l=1 (vb is an explicit output) → ,
  - m=0 (no internal unknowns)
  - only l=1 (explicit) equation:
- Voltage formulation, implicit
  - n=1; 2n = nIOs = 2
  - l=0 (no explicit output) →
  - m=0 (no internal unknowns)
  - only 1=n+m-l (implicit) equations:
- EE Network Interface Layer
  - nn = n+1 = 2 nodes
  - 2nn=4 NIF unknowns: nn=2 node voltages, nn=2 node currents:
  - n + nn= 3 equations:

---
Example: 2-terminal RCL block
- One way to do it
  - n=1; 2n = nIOs = 2
  - l=1 (1 explicit outputs) → ,
  - m=3 (3 internal unknowns):
  - l=1 explicit equations:
  - n+m-l=3 other (implicit) equations:
- EE Network Interface Layer
  - nn = n+1 = 2 nodes
  - 2nn=4 NIF unknowns: nn=2 node voltages, nn=2 node currents:
  - n + nn= 3 equations:

---
Example: 3-terminal RCLRC block
- One way to do it
  - n=2; 2n = nIOs = 4
  - l=2 (2 explicit outputs) → ,
  - m=2 (2 internal unknowns):
  - l=2 explicit equations:
  - n+m-l=2 other (implicit) equations:
- EE Network Interface Layer
  - nn = n+1 = 3 nodes
  - 2nn=6 NIF unknowns: nn=3 node voltages, nn=3 node currents:
  - n + nn= 5 equations:

---
Biochemical Reaction Networks and Devices
- “Nodes” == species (eg, A, B). Node vars: concs. ([A], [B])
- “Devices” == reactions
- “Branches” == which “nodes” involved in each reaction
  - arrow into reaction means:
    - conc. of “node” is used by reaction
  - arrow into node means:
    - reaction contributes term to “node's” dynamics
  - bidirectional (or no arrows) means both - this is typical
- “Devices” can have “internal nodes”
  - ie, private species that are not shared by other reactions
A
C
F
reaction 4
reaction 3
reaction 2
B
reaction 1
I
E
D

---
Example: Enzyme-Catalyzed Reaction “Device”
I/O
- : converts A (substrate) to D (product)
  - B is the enzyme/catalyst; C is the intermediate
- Rate equations:
  - n=2; 2n = nIOs = 4
    - : _d suffix for “device”
      - same idea as branch quantities (as opposed to node quantities)
  - l=2 (2 explicit outputs) → ,
  - m=2 (2 internal unknowns):
  - l=2 explicit equations:
  - n+m-l=2 other (implicit) equations:
[A]d
ECR
B
[D]d
C
dAdtd
dDdtd

---
ECR: Network Interface
- Reaction Network Interface Layer
  - relates “node/network quantities” and “branch/device quantities”
  - nn = n = 2 “nodes”: A, D
  - 2nn=4 NIL unknowns: nn=2 species ([A], [D]), nn=2 ddt terms: dAdt, dDdt
  - 2nn= 4 equations:
    - 2 “KCL contribs”:
    - 2 “KVL eqns”:
- Network level equations
  - at each “node” N (ie, for each species)
  - write 1 “KCL” equation:
    - 1 term for each “branch” connecting to “node”
  - “KVL”? Already taken care of at NIL level
F
dDdt2
dDdt1
D
dDdt3

---
Example: Michaelis-Menten-ECR “Device”
I/O
- : converts A (substrate) to D (product)
  - B is the enzyme/catalyst; C is the intermediate
- Michaelis-Menten approximation:
    - [B](0) == initial. conc. of the enzyme/catalyst
      - we will treat [B] as a (slowly-varying) species in the network
  - n=3; 2n = nIOs = 6
    - ; but and [D]d is not used
  - l=3 (3 explicit outputs) → ,
  - m=0 (no internal unknowns)
  - l=3 explicit equations:
  - n+m-l=0: no other equations
- Network Interface Layer
  - n=3 “KCL contribs”:
  - n=3 “KVL eqns”:
[A]d
MM-ECR
[D]d
dAdtd
dDdtd
[B]d

---
Example: “Species Source” Device
- : provides A
  - n=1; 2n = nIOs = 2
    - ; but [A]d is not used
  - l=1 (1 explicit output) → ,
  - m=0 (no internal unknowns)
  - l=1 explicit equation:
  - n+m-l=0: no other equations
- Network Interface Layer
  - n=1 “KCL contribs”:
  - n=1 “KVL eqns”:
dAdtd
A
source

---
Example: System “KCL” Equations for Two
Chained Enzyme-Catalyzed Reactions
B2
A
E
D
- A source supplies A (via rate of creation uA(t))
- ECR converts A to D
  - using “internal” species B1 (catalyst) and C (catalyst)
- MM-ECR converts D to E
  - using catalyst B2, supplied by B2 source
- Network-level “KCLs”:
  - A “KCL”:
  - D “KCL”:
  - B2 “KCL”:
  - E “KCL”:
dAdtAsrc
A
source
ECR
B1
C
dAdtECR
dDdtECR
dB2dtB2src
B2
source
MM-ECR
dDdtMM-ECR
dEdtMM-ECR

---
Chained ECR System: Unknown/Equation Counts
B2
A
E
D
- “MNA” formulation (eliminate “branch” quantities): size 6 system
  - unknowns: total 6
    - 4 network species: [A], [B2], [D], [E]
    - 2 internal species from ECR: [B1], [C]
  - equations: total 6
    - 4 network-level “KCL” equations (previous slide)
    - 2 internal equations from ECR (rate eqns. for [B1] and [C])
- Tableau formulation (keep all “branch” and “node” quantities)
  - unknowns: total 20
    - 4 “node” quantities == network species: [A], [B2], [D], [E]
    - Asrc: n=1 “branch” → 2n=2 unknowns (NIL's [A] and dAdt)
    - ECR: n=2 → 2n=4 unknowns (NIL's [A],[D],dAdt,dDdt)
      - plus: m=2 internal unknowns ([B1], [C])
    - B2src: n=1 “branch” → 2n=2 unknowns (NIL's [B2] and dB2dt)
    - MM-ECR: n=3 → 2n=6 unknowns (NIL's [A],[D],[B2],dAdt,dDdt,dB2dt)
  - equations: total 20
    - 4 “node KCLs” (previous slide)
    - Asrc: n=1 “branch” → 2n=2 equations (NIL's “KCL contrib” and “KVL” equations)
    - ECR: n=2 → 2n=4 equations (NIL's “KCL contrib” and “KVL” equations)
      - plus: m=2 internal equations (rate equations for [B1], [C])
    - B2src: n=1 “branch” → 2n=2 equations (NIL's “KCL contrib” and “KVL” equations)
    - MM-ECR: n=3 → 2n=6 equations (NIL's “KCL contrib” and “KVL” equations)
dAdtAsrc
A
source
ECR
B1
C
dAdtECR
dDdtECR
dB2dtB2src
B2
source
MM-ECR
dDdtMM-ECR
dEdtMM-ECR

---
Summary
- ModSpec: seed of a genuinely multi-domain simulator?
  - Xyce2?

---
translator
translator
translator
ModSpec MSL (Model Specification Language)
ModSpec
C++ API
ModSpec
Octave/MATLAB API
Simulation Outputs
(text+ GUI)
Commercial
& Industrial
Simulators
Xyce
DAEAPI + Algorithms
SPICE-compatible
Simulation Directives
Teaching
SPICE-compatible
 Netlists
Other
Open-Source
Simulators
SUGAR
nano-mechanical
structures
Verilog A CME
transistor-like
SBML
eg, chemical
sensors, “energy”
   lasers
optical
interconnect
nano-resonators

---
translator
translator
translator
Internal Parse Tree (fully general)
“Verilog-A Parser
to ModSpec”
translation, optimization,
derivative code generation, etc.
Xyce
Internal Data Structure for Model Eqns (f/q/etc.)
output translator
output translator
ModSpec
C++
SimKit
C?
ModSpec MATLAB
MDE
SUGAR
nano-mechanical
structures
Verilog A CME
transistor-like
SBML
eg, chemical
sensors, “energy”
   lasers
optical
interconnect
nano-resonators

---
Multi-physics support in Xyce
through ModSpec
translator
translator
translator
ModSpec C++ and .so files
Xyce
SUGAR
nano-mechanical
structures
Verilog A CME
transistor-like
SBML
eg, chemical
sensors, “energy”
   lasers
optical
interconnect
nano-resonators

---
Using ModSpec Devices in Xyce
updated 2012/11/06
[Speaker Notes: Notes here]