What is a “device”: version 0
- Something you give inputs to, to get outputs
  - n inputs n outputs
- Examples
  - resistor: n=1. or
  - capacitor/inductor: n=1. ,
  - : n=2.
input
output
+
-
+
inputs
outputs
[Speaker Notes: - Tianshi: 1) put anotther cap in parallel with resistor or better, 2) go straight to a SH model here. - then run SH in model exerciser]

---
What is a “device”: vers. 0 (contd.)
- In general:
  - n inputs:
  - n outputs:
  - n differential equations providing the outputs:
- But this cannot handle implicit formulations
  - ie, i-v relationships like this:
    - input/output distinction unclear
[Speaker Notes: - can access in model exerciser: MOD.qe, MOD.fe - diode-connected FEFET? Yes – use Gokcen's homotopy plot - hands on: just repeat last time's – doesn't have to be hands on, either, just a demo]

---
What is a “device”: version 1
- Lump inputs/outputs together: “IOs”
  - 2n IOs:
  - n implicit equations:
  - Key feature
    - if you specify n of the IOs, the other n can be solved for
      - more generally: if you supply n more equations in
- Example
  - n=1: , ,
- But then how do you express:
  - need internal unknowns
note abuse of notation: should be
[Speaker Notes: - examples are from a ckts background; better to update to parasitics on a device]

---
What is a “device”: version 2
- Augment IOs with internal unknowns
  - 2n IOs:
  - add m internal unknowns:
- To retain key property, need m more equations
  - we already had n equations in the IOs
    - generalize: make them depend on both and
  - add m more equations (1 per internal unk.)
[Speaker Notes: - explain this using an RRAM template - ipn = f1(vpn, s) - ds/dt = f2(vpn, s), eg, cubic - this will make it easier to get to the RRAM later]

---
What is a “device”: version 2 (cont.)
- Example:
  - n=2; 2n IOs =
  - Internal unks.: branch voltage and current of L
    - m=2; m int. unks. =
  - Equations
    - n=2 eqns. for IOs:
    - m=2 eqns. for int. unks.:
+
+
-
+
-

---
What is a “device”: version 3
- Support for “explicit outputs”
  - eventually, will want to set up KCL network eqns.
  - if (e.g.) currents are available explicitly, MNA does not need them as system unknowns
    - want a way to specify outputs that are available explicitly
- Previous example: n=2, m=2
    - equations are all implicit
    - note: IOs i1 and i2 are available explicitly
+
+
-
+
-

---
What is a “device”: version 3 (contd.)
- Re-write previous example (n=m=2)
  - 2n IOs = v1, v2, i1, i2
    - denote i1, i2 as explicit outputs:
    - denote remaining IOs as “otherIOs”:
  - Write equations for the explicit outputs
  - Write remaining eqns. (don't use explicit outputs)
+
-
+
-
+
[Speaker Notes: - Juan-Pablo: why not make w() a function of z as well? Seems no flip side, and can make equation writing more compact and less error prone.]

---
What is a “device”: version 3 (contd.)
- Explicit output support: the general case
  - 2n IOs, split into:
    - l explicit outputs (0 <= l <= n):
    - 2n-l “otherIOs”:
  - m internal unknowns:
  - l equations for the explicit outputs
  - n+m-l remaining (implicit) equations
[Speaker Notes: - example: just continue with the RRAM pattern, no need to have explicit outputs; they have already seen that. - have a small exercise for the MVS model – count number of equations and unknowns.]

---
What is a “device”: version 4
- Support for independent sources
- Previous example w/ 2 indep. sources
  - voltage source
  - current source
- Equations now involve :
+
-
+
-
+
[Speaker Notes: - motivate using not only vsrc/isrc, but also RRAM, which can, eg, have a noise voltage source – but it should be declared as a voltage source, then noise part (Monte-Carlo sample) should be attached in the simulator. - so continue with the RRAM pattern. - NEVER include any random number generation inside your model (that should be done at the simulator level) - NEVER even attach deterministic time domain sources – also at the simulator level.]

---
What is a “device”: finally
- 2n IOs, split into:
  - l explicit outputs (0 <= l <= n):
  - 2n-l “otherIOs”:
- m internal unknowns:
- independent sources:
- l equations for the explicit outputs
- n+m-l remaining (implicit) equations

---
Describing a device: ModSpec
- Look through, eg, resModSpec.m
  - pulls in ModSpec_common_skeleton, which pulls in:
    - ModSpec_skeleton_core (defines API - field names)
      - uniqID, name, ModelName, description, ...
      - parmnames, parmdefaults
      - IOnames
      - ExplicitOutputNames: (“vecZ”)
      - InternalUnknames: (“vecY”)
      - ImplicitEquationNames: (“vecW”)
      - uNames: (“vecU”)
      - otherIOnames: (“vecX”)
      - fe, fi, qe, qi: functions
        - note: dependence of on not supported yet
      - NIL (Network Interface Layer): to be discussed later
    - ModSpec_common_add_ons, ModSpec_derivative_add_ons
      - these set up default values for data, define utility functions, set up functions to perform automatic differentiation (AD) using vecvalder
        - AD used for obtaining Jacobians of
[Speaker Notes: - next time: some slides on vecvalder?]

---
 Describing a ModSpec device (contd.)
- Network Interface Layer (NIL)
  - list of nodes (NIL.node_names)
    - eg, {'n1', 'n2'}
    - reference node (NIL.refnode_name) - eg, 'n3'
  - IOs are defined from these
    - v/i branches from each
    - node to refnode
    - syntax:
      - v<node><refnode>,
      - i<node><refnode>
        - all voltages first,
        - then all currents
      - eg.: {'vn1n3',
      - 'vn2n3', 'in1n3',
      - 'in2n3'}
  - explicit outputs are
  - a subset of these
    - eg: {'in1n3', 'vn2n3'}
Network
Level
Network Interface Layer
(domain-specific: eg, EE-NIL has nodes)
refnode
n1
n2
n3
Core Device
generic, not just EE

---
 Describing a ModSpec device (contd.)
- resModSpec.m (contd.)
  - set up data (API functions use these):
    - model_name, spice_key, model_description
    - parm_names (“R”), parm_defaultvals, parm_types (double/int/string), parm_vals (current parameter values)
    - NIL.node_names (“p”,”n”), NIL.refnode_name (“n”)
    - explicit_output_names (“ipn”)
    - setup_IOnames_OtherIOnames_IOtypes_IOnodenames() sets up IOnames (“vpn, “ipn”), OtherIOnames (“vpn”)
      - and book-keeping information IOtypes (“v”/”i”), IOnodenames (tells which node an IO corresponds to)
    - internal_unk_names, implicit_equation_names
      - empty for resistors
    - u_names (empty for resistors)
  - Define fe, fi, qe, qi
    - vecZ = fe(vecX, vecY, vecU) = vpn/R
    - qe, fi, qi: empty for resistor

---
Example: writing a ModSpec model
- Previous example
  - demo:
    - copy resModSpec and modify
      - work around not supporting
      - work around vecvalder “bug”
    - test functions using run_Model_API
+
-
+
-
+
[Speaker Notes: - because qie don't support u args, need to declare an extra y variable - vE and add an extra equation: EbCR - there was a vecvalder problem: first entry of a vector was 0, need to do that second, or make the first entry dependent on every unknown (eg, fqout(1,1)=0*x1 + 0*x2 + 0*x3, etc.. Alert them to it.]

---
Netlists in MATLAB: circuitdata
- circuitdata: a format/data structure for describing electrical networks (“netlists”)
  - using ModSpec models
- fields of circuitdata:
  - cktname (string)
    - eg.: 'my circuit'
  - nodenames (cell array of strings - all node names)
    - eg.: {'n1', 'n2', 'n3'}
    - do not include the ground node (BUG?)
  - groundnodename (string)
    - eg.: 'mygnd'
  - elements (cell array of structures for each element)
    - eg.: {ResElem1, RLCsrcsElem1, VinElem1}

---
Netlists in MATLAB (contd.)
- structure for each element: the fields
  - name (string)
    - eg.: 'Vin1'
  - model (the ModSpec model (MOD))
    - eg.: Vin1Elem.model = vsrcModSpec();
  - nodes (cell array of nodes connected to)
    - same order as in ModSpec description
    - eg.: Vin1Elem.nodes = {'n1', 'mygnd'}
  - parms (cell array of parameter values for model)
    - same order as parm names in ModSpec description
    - eg.: resElem1.parms = {100.0}; % R
  - udata (cell array of structures describing values)
    - eg.: RLCsrcsElem1.udata = {E_udata, I_udata};
    - must be in the same order as ModSpec uNames

---
Netlists in MATLAB (contd.)
- fields of the udata entry structures
  - uname (string)
    - must be exactly the name of the u source in ModSpec
    - eg.: E_udata.uname = 'E';
  - QSSval (QSS/DC value)
    - e.g: E_udata.QSSval = 1.0;
  - utransient (fn. handle for transient analysis input)
    - similar to DAEAPI functions, but scalar
    - e.g: E_udata.utransient = @(t, args) sin(2*pi*args.f*t);
  - utransientargs (args for utransient)
    - eg.: args.f=1e3; E_udata.utransientargs = args;
  - uLTISSS (fn. handle for AC analysis input)
    - similar to DAEAPI functions, but scalar
    - e.g: E_udata.uLTISSS = @(f, args) args.ACr + args.ACi i;
  - uLTISSSargs (args for uLTISSS)
    - eg.: args.r=1; args.i=0; E_udata.uLTISSSargs = args;

---
Netlists in MATLAB: an example
- demo
  - write the circuitdata structure in MATLAB
  - run/test/debug it
'1'
I1
'2'
X1
L1
'3'
'4'
R1
X2
'gnd'

---
Making a DAE from circuitdata
- MNA_EqnEngine
  - takes a circuitdata structure, returns a DAE
    - DAE = MNA_EqnEngine(circuitdata);
- Demo
  - DAE fields
    - standard DAEAPI functions (see DAEAPI documentation)
      - eg., DAE.f(), DAE.q(), DAE.dfdx(), etc.
    - which rely on an internal data structure
      - eg.: unk_names, eqn_names, element_names, input_names, parm_names, *_updates, etc.
    - you should use ONLY the API functions when using DAE
      - see the documentation
  - test the DAE: run_DAEAPI_functions(DAE)

---
Running Analyses on the DAE
QSS (DC)
    - qss = QSS(DAE);
    - n = feval(DAE.nunks, DAE);
    - NRguess = zeros(n,1); %bad guess! try to do better
    - qss = feval(qss.solve, NRguess, qss);
    - feval(qss.print, qss);
LTISSS (AC) - do a QSS first
  - don't forget to set AC inputs first
  - outputs = StateOutputs(DAE);%to plot all state vars
  - DCus = feval(DAE.uQSS, DAE); % DC input vals
  - DCsol = feval(qss.getsolution, qss);
  - AC = LTISSS(DAE, DCsol, DCus);
  - sweeptype = 'DEC'; % decade plot
  - fstart=1; fstop=1e12; nsteps=5;% 5 pts/decade
  - AC=feval(AC.solve, fstart, fstop, nsteps, sweeptype, AC);
  - feval(AC.plot, AC, outputs);

---
Running Analyses on the DAE (contd.)
- Transient (LMS)
  - TrBE = LMS(DAE); % default method is BE
    - TRmethods = LMSmethods(); % defines FE, BE, TRAP, GEAR2
    - TRparms = defaultTranParms(); % has, eg, TRparms.NRparms
    - TrGEAR2= LMS(DAE, TRmethods.GEAR2, TRparms); %GEAR2
  - Trans = TrBE;
    - Trans.tranparms.stepControlParms.doStepControl=0;
  - xinit = DCsol; % DC solution
  - tstart=0; tstep=1e-9; tstop=1e-7;
  - Trans = feval(Trans.solve, Trans, xinit, tstart, tstep, tstop);
  - [thefig,legends] = feval(Trans.plot, Trans, outputs);
- Watch out for tiny +ve eigenvalues due to DAEs and finite-precision numerics!
  - demo (TRAP/small timesteps/random ICs; illustrative example)
  - use overstable integration methods (BE, GEAR2)
  - use timesteps consistent with real eigenmodes
    - helps integration method damp out spurious eigenmodes (too-small timesteps can excite them)
[Speaker Notes: - MAPP-0.0.3 transient has a bug - it does not clear tpts/vals at the start of solve - random init conds, TRAP, small timesteps fail on the circuit - it goes unstable! - the reason is DAEs + finite precisionnumerics: it makes zero eigenvalues (from DAEs) into very high-frequency poles (ie, very small eigenvalues) with random sign - ie, the circuit can easily turn unstable. This is easy to demonstrate by hand using a simple 3x3 LTI circuit and doing an eigenanlysis - you get tiny eigenvalues whose sign depends randomly on element values etc.. You can also see this from eig(inv(AC.Gmat)*AC.Cmat), of course. - see [xournal-notes]/2013-01-30-Note-05-28-simpleDAE-eigenstability-debug.xoj for the circuit - the “fix”: - use overstable methods like BE and TRAP - don't use too-small timesteps]

---
Organization of the Code
- MAPP (Model/Algorithm Prototyping Platform)
  - enables you to write a model in ModSpec
    - automatic differentiation facility using vecvalder
  - describe simple circuits using circuitdata and MNA_EqnEngine
    - + define your own DAEs in DAEAPI
    - vecvalder-based AD available at the DAE level, too
  - DC/AC/transient/etc. analyses supplied
    - can write your own analyses
  - completely in MATLAB/Octave
- MAPP consists of 4 components
  - vecvalder: automatic differentiation in MATLAB
  - ModSpec: model specification in MATLAB
  - DAEAPI: set up circuit DAEs from circuitdata
  - A1oDAEAPI: basic analyses (DC/AC/transient)
    - “Analyses-1 on DAEAPI”

---
“Real” Model Description Languages
- Verilog-A(MS); VHDL-AMS; MAST Saber/Synopsys; Modelica/Dymola (thanks → David Smith, Synopsys)
  - these are high-level languages (higher than ModSpec)
    - not “directly executable”
    - (don't work in MATLAB/Octave)
    - (ModSpec is a low-level API: functions directly callable by simulation/equation engines)
  - toolchains (mostly) closed or commercial
    - exception: Modelica (but issues compiling/using the open-source version)
    - exception: Verilog-A (?)
      - ADMS: no longer open source; buggy
  - general-purpose languages
    - typically many more capabilities than needed for CT device model description
      - == rope to hang yourself?

---
EE Networks: A Quick Recap
- EE Network Layer
  - nodes
    - there is a special node called ground
  - devices connect to nodes using branches
  - network-level unknowns
    - each non-ground node contributes one node voltage unknown
    - each branch contributes (in principle):
      - one branch current unknown
      - one branch voltage unknown
        - directions indicate current direction and branch voltage polarity
  - network-level equations
    - each non-ground nodes contributes one KCL equation
      - eg, KCLN:
    - each branch contributes one KVL equation:
      - (each branch also contributes one BCR equation – from the device layer)
- EE device layer
  - each can contribute several branches (connected to network-level nodes)
    - devices have access to network-level branch quantities ONLY
  - each device contributes one BCR equation for each of its branches:

---
A Generic Device (not limited to EE)
Device's Network Interface Layer
(interfaces device to network level)
Network
Level
n3
n1
n2
Network interface layer interfaces “network quantities” (eg, node voltages, node KCL current contribs) with “device quantities” (eg, branch voltages and currents)
Core Device
(eg, only branch
quantities and
int. quantities)

---
Core vs NIL vs Network Level
- Core device
  - relates (its own) branch voltages and currents (I/Os)
    - ie, supplies equations relating branch voltages/currents
  - may also contribute internal unknowns
    - these don't interact with network level quantities
    - for each internal unknown, device supplies one equation
- Network Level
  - contributes node voltage unknowns
  - sets up KCL equations for each node
    - using each device's Network Interface Layer
- Network Interface Layer
  - relates core device's I/Os (branch voltages/currents) to network level quantities (node voltages, node KCL contribs)
  - does not access core device's internal unknowns
Network Level
n1
3 nodes/KCL eqns
2 KVL eqns
n2
4 I/Os
2 eqns
Network Interface
Layer
3 device I/O to network KCL contrib. eqns
3 node KCL contribs.
3 node voltages
n3
Core
2 branches

---
Core Device: Basic Notions
- Each device:
  - has several inputs/outputs; some outputs provided explicitly, others implicit
  - contributes several internal unknowns
  - contributes several equations
- IOs: these are the Inputs/Outputs
  - 2n of them. (What is n? # of “core I/O eqns”; eg, # branches)
    - l of these can be designated ExplicitOutputs
      - stored in
    - the remaining 2n-l are called OtherIOs
      - stored in
- There can also be m InternalUnknowns (stored in )
- Equations: total of n+m equations supplied by device
    - l of these provide the ExplicitOutputs explicitly:
      - l equations: : qe(), fe()
    - the remaining n+m-l equations can be fully implicit:
      - n+m-l equations: : qi(), fi()
    - is a vector of time-varying functions, of length

---
Example: Resistor
- Explicit current output formulation
  - n=1; 2n = nIOs = 2
  - l=1 (ib is an explicit output) → ,
  - m=0 (no internal unknowns)
  - only 1 (explicit-output) equation:
- Implicit current formulation
  - n=1; 2n = nIOs = 2
  - l=0 (ib is implicit) →
  - m=0 (no internal unknowns)
  - only 1 (implicit) equation:
- EE Network Interface Layer
  - nn = n+1 = 2 nodes

---
Example: Capacitor (charge formulation)
- Charge formulation, explicit output
  - n=1; 2n = nIOs = 2
  - l=1 (qb is an explicit output) → ,
  - m=0 (no internal unknowns)
  - only l=1 (explicit) equation:
- Charge formulation, implicit
  - n=1; 2n = nIOs = 2
  - l=0 (no explicit output) →
  - m=0 (no internal unknowns)
  - only n+m-l=1 (implicit) equations:
- EE Network Interface Layer
  - nn = n+1 = 2 nodes
  - 2nn=4 NIF unknowns: nn=2 node voltages, nn=2 node currents:
  - n + nn= 3 equations:

---
Example: Capacitor (current formulation)
- Current formulation, explicit output
  - n=1; 2n = nIOs = 2
  - l=1 (qb is an explicit output) → ,
  - m=0 (no internal unknowns)
  - only l=1 (explicit) equation:
- Current formulation, implicit
  - n=1; 2n = nIOs = 2
  - l=0 (no explicit output) →
  - m=0 (no internal unknowns)
  - only n+m-l=1 (implicit) equations:
- EE Network Interface Layer
  - nn = n+1 = 2 nodes
  - 2nn=4 NIF unknowns: nn=2 node voltages, nn=2 node currents:
  - n + nn= 3 equations:

---
Example: Inductor (flux formulation)
- Flux formulation, explicit output
  - n=1; 2n = nIOs = 2
  - l=1 (fb is an explicit output) → ,
  - m=0 (no internal unknowns)
  - only l=1 (explicit) equation:
- Flux formulation, implicit
  - n=1; 2n = nIOs = 2
  - l=0 (no explicit output) →
  - m=0 (no internal unknowns)
  - only n+m-l=1 (implicit) equations:
- EE Network Interface Layer
  - nn = n+1 = 2 nodes
  - 2nn=4 NIF unknowns: nn=2 node voltages, nn=2 node currents:
  - n + nn= 3 equations:

---
Example: Inductor (voltage formulation)
- Voltage formulation, explicit output
  - n=1; 2n = nIOs = 2
  - l=1 (vb is an explicit output) → ,
  - m=0 (no internal unknowns)
  - only l=1 (explicit) equation:
- Voltage formulation, implicit
  - n=1; 2n = nIOs = 2
  - l=0 (no explicit output) →
  - m=0 (no internal unknowns)
  - only 1=n+m-l (implicit) equations:
- EE Network Interface Layer
  - nn = n+1 = 2 nodes
  - 2nn=4 NIF unknowns: nn=2 node voltages, nn=2 node currents:
  - n + nn= 3 equations:

---
Example: 2-terminal RCL block
- One way to do it
  - n=1; 2n = nIOs = 2
  - l=1 (1 explicit outputs) → ,
  - m=3 (3 internal unknowns):
  - l=1 explicit equations:
  - n+m-l=3 other (implicit) equations:
- EE Network Interface Layer
  - nn = n+1 = 2 nodes
  - 2nn=4 NIF unknowns: nn=2 node voltages, nn=2 node currents:
  - n + nn= 3 equations:

---
Example: 3-terminal RCLRC block
- One way to do it
  - n=2; 2n = nIOs = 4
  - l=2 (2 explicit outputs) → ,
  - m=2 (2 internal unknowns):
  - l=2 explicit equations:
  - n+m-l=2 other (implicit) equations:
- EE Network Interface Layer
  - nn = n+1 = 3 nodes
  - 2nn=6 NIF unknowns: nn=3 node voltages, nn=3 node currents:
  - n + nn= 5 equations:

---
Biochemical Reaction Networks and Devices
- “Nodes” == species (eg, A, B). Node vars: concs. ([A], [B])
- “Devices” == reactions
- “Branches” == which “nodes” involved in each reaction
  - arrow into reaction means:
    - conc. of “node” is used by reaction
  - arrow into node means:
    - reaction contributes term to “node's” dynamics
  - bidirectional (or no arrows) means both - this is typical
- “Devices” can have “internal nodes”
  - ie, private species that are not shared by other reactions
A
C
F
reaction 4
reaction 3
reaction 2
B
reaction 1
I
E
D

---
Example: Enzyme-Catalyzed Reaction “Device”
I/O
- : converts A (substrate) to D (product)
  - B is the enzyme/catalyst; C is the intermediate
- Rate equations:
  - n=2; 2n = nIOs = 4
    - : _d suffix for “device”
      - same idea as branch quantities (as opposed to node quantities)
  - l=2 (2 explicit outputs) → ,
  - m=2 (2 internal unknowns):
  - l=2 explicit equations:
  - n+m-l=2 other (implicit) equations:
[A]d
ECR
B
[D]d
C
dAdtd
dDdtd

---
ECR: Network Interface
- Reaction Network Interface Layer
  - relates “node/network quantities” and “branch/device quantities”
  - nn = n = 2 “nodes”: A, D
  - 2nn=4 NIL unknowns: nn=2 species ([A], [D]), nn=2 ddt terms: dAdt, dDdt
  - 2nn= 4 equations:
    - 2 “KCL contribs”:
    - 2 “KVL eqns”:
- Network level equations
  - at each “node” N (ie, for each species)
  - write 1 “KCL” equation:
    - 1 term for each “branch” connecting to “node”
  - “KVL”? Already taken care of at NIL level
F
dDdt2
dDdt1
D
dDdt3

---
Example: Michaelis-Menten-ECR “Device”
I/O
- : converts A (substrate) to D (product)
  - B is the enzyme/catalyst; C is the intermediate
- Michaelis-Menten approximation:
    - [B](0) == initial. conc. of the enzyme/catalyst
      - we will treat [B] as a (slowly-varying) species in the network
  - n=3; 2n = nIOs = 6
    - ; but and [D]d is not used
  - l=3 (3 explicit outputs) → ,
  - m=0 (no internal unknowns)
  - l=3 explicit equations:
  - n+m-l=0: no other equations
- Network Interface Layer
  - n=3 “KCL contribs”:
  - n=3 “KVL eqns”:
[A]d
MM-ECR
[D]d
dAdtd
dDdtd
[B]d

---
Example: “Species Source” Device
- : provides A
  - n=1; 2n = nIOs = 2
    - ; but [A]d is not used
  - l=1 (1 explicit output) → ,
  - m=0 (no internal unknowns)
  - l=1 explicit equation:
  - n+m-l=0: no other equations
- Network Interface Layer
  - n=1 “KCL contribs”:
  - n=1 “KVL eqns”:
dAdtd
A
source

---
Example: System “KCL” Equations for Two
Chained Enzyme-Catalyzed Reactions
B2
A
E
D
- A source supplies A (via rate of creation uA(t))
- ECR converts A to D
  - using “internal” species B1 (catalyst) and C (catalyst)
- MM-ECR converts D to E
  - using catalyst B2, supplied by B2 source
- Network-level “KCLs”:
  - A “KCL”:
  - D “KCL”:
  - B2 “KCL”:
  - E “KCL”:
dAdtAsrc
A
source
ECR
B1
C
dAdtECR
dDdtECR
dB2dtB2src
B2
source
MM-ECR
dDdtMM-ECR
dEdtMM-ECR

---
Chained ECR System: Unknown/Equation Counts
B2
A
E
D
- “MNA” formulation (eliminate “branch” quantities): size 6 system
  - unknowns: total 6
    - 4 network species: [A], [B2], [D], [E]
    - 2 internal species from ECR: [B1], [C]
  - equations: total 6
    - 4 network-level “KCL” equations (previous slide)
    - 2 internal equations from ECR (rate eqns. for [B1] and [C])
- Tableau formulation (keep all “branch” and “node” quantities)
  - unknowns: total 20
    - 4 “node” quantities == network species: [A], [B2], [D], [E]
    - Asrc: n=1 “branch” → 2n=2 unknowns (NIL's [A] and dAdt)
    - ECR: n=2 → 2n=4 unknowns (NIL's [A],[D],dAdt,dDdt)
      - plus: m=2 internal unknowns ([B1], [C])
    - B2src: n=1 “branch” → 2n=2 unknowns (NIL's [B2] and dB2dt)
    - MM-ECR: n=3 → 2n=6 unknowns (NIL's [A],[D],[B2],dAdt,dDdt,dB2dt)
  - equations: total 20
    - 4 “node KCLs” (previous slide)
    - Asrc: n=1 “branch” → 2n=2 equations (NIL's “KCL contrib” and “KVL” equations)
    - ECR: n=2 → 2n=4 equations (NIL's “KCL contrib” and “KVL” equations)
      - plus: m=2 internal equations (rate equations for [B1], [C])
    - B2src: n=1 “branch” → 2n=2 equations (NIL's “KCL contrib” and “KVL” equations)
    - MM-ECR: n=3 → 2n=6 equations (NIL's “KCL contrib” and “KVL” equations)
dAdtAsrc
A
source
ECR
B1
C
dAdtECR
dDdtECR
dB2dtB2src
B2
source
MM-ECR
dDdtMM-ECR
dEdtMM-ECR

---
translator
translator
translator
ModSpec MSL (Model Specification Language)
ModSpec
C++ API
ModSpec
Octave/MATLAB API
Simulation Outputs
(text+ GUI)
Commercial
& Industrial
Simulators
Xyce
DAEAPI + Algorithms
SPICE-compatible
Simulation Directives
Teaching
SPICE-compatible
 Netlists
Other
Open-Source
Simulators
SUGAR
nano-mechanical
structures
Verilog A CME
transistor-like
SBML
eg, chemical
sensors, “energy”
   lasers
optical
interconnect
nano-resonators

---
Using ModSpec Devices in Xyce
updated 2012/11/06
[Speaker Notes: Notes here]