VAPP: Instructions for Hands-On Examples

1. Setup MAPP + VAPP:

By now you should have a working MAPP + VAPP setup on your machine. If not, get one of us (Archit, Tianshi, Gokcen or Jaijeet) to help you.

2. Run a Full-Blown Test Script:

At a MATLAB prompt: run the FEFET test script by typing the following:

Change into workshop directory:	cd workshop
Change into Alam_FEFET directory:	cd Alam_FEFET
Translate the FEFET model:	va2modspec('mvs_5t_mod2.va')
Calculate characteristic curves with MAPP:	run_char_curves_Alam_fefet_combined

3. Go back to basics – Create your own VA model and import it into MAPP using VAPP

Go to the “diode” directory under the workshop sub-directory in your VAPP installation and follow these steps in order to implement a simple diode Model in Verilog-A and import in into VAPP.

Simple diode

Open the “diode.va” file and find

I(br_dio) <+

statement on line 16.
Compete the missing RHS of the contribution statement with

 Is * (exp((V(br_dio))/$vt(Temp)) – 1);

Import the diode model into MAPP

va2modspec('diode.va');

Compute the IV-curve of the diode by running

run_char_curves_diode;

The script will ask you to connect sources to the terminals of the device.

Choose V or I for terminal p. [V]:

type V ⏎

Choose V or I for terminal n. [V]:

type V ⏎

You should see the I-V curve of the diode now.

Now edit the file “run_char_curves_diode.m”
Change the voltage value in line 5 from 0.7 to 1

Vhigh = 1;

Run the IV-curve calculation again:

run_char_curves_diode;

- MAPP should quit and display an error.
  What is the reason?
Resistor + Diode

  - Add an internal node, int, to your model at line 7

electrical p, int, n;

Connect the second node of the br_dio branch to the internal node
and add a second branch, br_res

branch(p, int) br_dio;
    branch(int, n) br_res;

Add the resistor equation to your model

I(res) <+ V(res)/R;

Import the new diode model into MAPP

va2modspec('diode.va');

Try running the transient analysis with the new model

run_char_curves_diode;

4.	Ferro-electric FET

A ferro-electric FET is a transistor with a gate capacitance that has negative capacitance	regions.

To investigate this behavior:

Cd into the Alam_FEFET directory

Translate the two models

va2modspec('mvs_5t_mod.va');
va2modspec('neg_cap_3t.va');

Compute the non-linear charge-voltage characteristic of the negative capacitance device
run_dcsweep_neg_cap_3t;

Run the homotopy analysis

run_char_curves_Alam_fefet;

Run the analysis on the simple inverter circuit involving a FEFET

  run_inverter_homotopy_Alam_fefet;

5. Bsim3 Ring Oscillator

Go to the bsim3_ringosc directory and translate the BSIM model. After that you can run the	run_transient_bsim3_ringosc script to perform a transient simulation and see the	oscillatory behavior of the circuit.
This can take a long time. You can explore the model and the simulation script while we wait.

6. VALint

At any time during the workshop, you may access VALint tool at

https://nanohub.org/resources/vachecker.

VALint is the NEEDS created, automatic Verilog-A code checker to check the quality of the Verilog-A code and provide the author feedback if bad practices, common mistakes, pitfalls, or inefficiencies are found.